ESP32 & IoT
Alberto

---
ESP32 module

---
ESP32 - inside
Processore Tensilica LX6 dual core a 240 MHz
- 520Kb di memoria SRAM
- Connettività wifi 802.11 b/g/n (supporto per WEP, WPA/WPA2 PSK/Enterprise)
- Connettività Bluetooth (classica e LE)
- 32 PIN di I/O con diverse periferiche disponibili
- accelerazione hardware per algoritmi di sicurezza (AES, SHA2, RSA-4096)

---
Processore Tensilica LX6 dual core a 240 MHz
- Architecture RISC 32-bits Little-endian
- 24/16-bit instructions
- 64 general purpose registers with 16 visible registers
- Dual/single -core
- 240 MHz maximum frequency

---
BENCHMARK RESULTS
(smaller values are better)
        float [ms] int32[ms]
Arduino uno @16MHz 3326	4446
ESP8266 @160MHz 216 28
ESP32 @240MHz 95 3

---
ESP32 MEMORY
- ROM 448 KiB (boot & core )
- SRAM 520 KiB - data & program
- RTC Fast RAM 8 KiB - data
- RTC slow RAM 8 KiB - use in deep sleep mode
- eFUSE 1 KiB ( 256 bit MAC & config - 768 user)
- FLASH:
- 0 Mib ESP32-D0WDQ6 -D0WD -S0WD(singlecore)
- 2 MiB ESP32-D2WD
- 4 MiB ESP32 PICO D4

---
WiFI
- Supports sniffer, Station, SoftAP and Wi-Fi direct mode
- Max data rate of 150 Mbps@11n HT40, 72 Mbps@11n HT20, 54 Mbps@11g, and 11 Mbps@11b
- Maximum transmit power of 19.5 dBm@11b, 16.5 dBm@11g, 15.5 dBm@11n
- Minimum receiver sensitivity of -97 dBm
- 135 Mbps UDP sustained throughput

---
Varianti Espressif

---
Programmazione
- Pc ( Linux - Windows – Mac)
- Editor (eclipse)
- Toolchain Espressif ( linguaggio C )
  git clone --recursive https://github.com/espressif/esp-idf.git
- Cavo usb

---
Linguaggi e SDK
- Arduino IDE with the ESP32 Arduino Core
- ESP Easy – developed by home automation
- Espruino – JavaScript SDK emulating Node.js
- Lua RTOS for ESP32 or NodeMCU
- Mongoose OS – JavaScript or C. AWS IoT, and Google Cloud IoT.
- mruby for the ESP32
- MicroPython

---
Programmazione semplificata
- Installare IDE arduino
- Installare i Board add-on https://dl.espressif.com/dl/package_esp32_index.json into the “Additional Board Manager URLs
- Installare le eventuali librerie per ESP32
- (https://randomnerdtutorials.com/installing-the-esp32-board-in-arduino-ide-windows-instructions)

---
librerie

---
Over The Air programming

---
OTA

---
ESP32 SPIFF
- The ESP32 contains a Serial Peripheral Interface Flash File System (SPIFFS).
- Create configuration files with settings;
- Save data permanently;
- Create files to save small amounts of data instead of using a microSD card;
- Save HTML and CSS files to build a web server;

---
Moduli base

---
Moduli USB

---
ESP32 + SD card

---
ESP32 + batteria

---
ESP32 + OLED

---
ESP32 + LoRa +GPS

---
ESP32 camera + PIR + Oled 64x128

---
M5 Stack

---
Consigli per gli acquisti
- SE costa troppo poco …. a volte non funziona
- Ma e' dual core o single core ?
- Quanta memoria flash ha realmente ? ( non quanta ne supporta o potrebbe montarne)
- Se lo dovete alimentare a batterie evitate gli accessori inutili ( USB LED LCD … ) o spegneteli .
- Attenti ai falsi profeti ( traduttori improvvisati, youtuber cerca-click … )

---
Firmware self service
- Cosa trovate gia' pronto :
- https://github.com/arendst/Sonoff-Tasmota/wiki
- https://esphome.io/index.html
- https://github.com/1technophile/OpenMQTTGateway

---
IOT Home automation …. next

---
DEMO …

---
Link utili – SETUP
- https://forum.arduino.cc/index.php?topic=358374.0
- https://randomnerdtutorials.com/installing-the-esp32-board-in-arduino-ide-windows-instructions/
- https://www.instructables.com/id/IOT-Made-Simple-Playing-With-the-ESP32-on-Arduino-

---
Sitografia
- https://en.wikipedia.org/wiki/ESP32
- http://esp32.net/
  http://iot-bits.com/category/esp32-articles/
- https://www.esp32.com (english forum)
- https://leanpub.com/kolban-ESP32
- https://github.com/nkolban
- http://www.lucadentella.it/category/esp32/

---
Tutorial (inglese)
Andreas Spiess
https://www.youtube.com/channel/UCu7_D0o48KbfhpEohoP7YSQ
- Peter Scargill's Tech Blog
- https://tech.scargill.net/
- Florian 1technophile
- https://1technophile.blogspot.com/